## Slide 1
Tensile Membrane FSI
Partitioned Serial-Staggered Method — Step by Step
Fluid–structure interaction of prestressed fabric membranes in incompressible flow · tensile_membrane_fsi

## Slide 2
Agenda — What this deck covers
• Problem & modelling goal
• Partitioned vs monolithic FSI
• Code architecture & modules
• Setup: mesh, material, prestress, fluid grid
• One coupled time step — every sub-step
• Membrane dynamics (CST FEM + explicit integrator)
• Fluid solver (PISO-like + LES + immersed boundary)
• Load transfer modes
• Stabilisation knobs (damping, mass_scale, under-relaxation)
• Outputs, flutter case, and static DOLFINx contrast
Tensile Membrane FSI · Partitioned serial-staggered method · 2/26

## Slide 3
1. Problem statement
Part A
Physics
A thin prestressed tensile membrane
(sail / canopy / fabric roof) sits in a
3D air channel.
Flow exerts unsteady pressure → membrane
deforms and moves.
Membrane motion changes the flow
(immersed boundary) → two-way FSI.
Goal: capture transient interaction,
including flutter when damping is low.
Numerical approach in this repo
Membrane: CST triangles, prestress +
plane-stress elasticity, explicit CD.
Fluid: incompressible NS on Cartesian
grid, fractional-step / PISO-like,
optional Smagorinsky LES.
Coupling: partitioned serial staggered
(not monolithic).
IB: thin-band mask of fluid cells on the
membrane surface.
Tensile Membrane FSI · Partitioned serial-staggered method · 3/26

## Slide 4
2. Partitioned vs monolithic
Part A
This code = PARTITIONED
Fluid and structure are separate solvers.
Each time step:
1) advance fluid with current IB
2) transfer loads to membrane
3) advance membrane
4) update IB from new position
Optional under-relaxed sub-iterations
tighten the interface residual.
Config: scheme: serial_staggered
Monolithic (NOT used here)
Fluid + structure + interface assembled
into one joint algebraic system.
Solved together each step / Newton
iteration.
Stronger coupling / often more stable,
but larger, more complex Jacobian and
harder to reuse separate solvers.
Your DOLFINx SNES script is membrane-
only static analysis — neither FSI style.
Tensile Membrane FSI · Partitioned serial-staggered method · 4/26

## Slide 5
3. Repository architecture
Part A
• main.py — load YAML, build FSISimulation, run loop, save outputs
• config/default.yaml | flutter.yaml — physics & numerics
• src/membrane/ — geometry (CST mesh), materials, prestress / form-finding, explicit solver
• src/fluid/ — Cartesian grid, PISO-like NS, Smagorinsky LES
• src/fsi/ — coupling driver, load transfer, immersed-boundary update
• src/utils/ — YAML I/O, NPZ/VTK writers, plots, GIF helpers
• examples/ — membrane-only, coarse FSI, flutter GIF, Gmsh generator
• tests/ — unit / smoke checks for membrane and coupled step
Tensile Membrane FSI · Partitioned serial-staggered method · 5/26

## Slide 6
4. Setup pipeline (before time stepping)
Part B
A
Build rectangular CST membrane mesh + fixed-edge BCs
B
Apply slight analytical sag so flow sees a curved sail
C
Create MembraneMaterial (E, ν, thickness, prestress)
D
Dynamic-relaxation prestress (heavily damped) → equilibrium
E
Restore user transient damping from config
F
Build FluidGrid + FluidSolver (ρ, ν, U_inlet, LES flags)
G
Initial immersed-boundary mask from membrane state
H
Read FSI knobs: α, max_subiters, load_mode, load_scale
Tensile Membrane FSI · Partitioned serial-staggered method · 6/26

## Slide 7
5. Membrane mesh & BCs
Part B · Setup A–B
• Rectangular patch in a reference plane; discretised into constant-strain triangles (CST)
• Config: length, width, nx, ny → node/element connectivity
• Placement in fluid: membrane_x0, membrane_y0, membrane_z0
• fixed_edges (e.g. left/right/bottom/top) → Dirichlet nodes held at reference
• initial_sag_shape: sinusoidal z-displacement so the sail is not perfectly flat
• Why sag? A flat zero-curvature start has weak geometric stiffness and is a poor IB seed
• Geometry helpers recompute element areas and normals as the membrane moves
Tensile Membrane FSI · Partitioned serial-staggered method · 7/26

## Slide 8
6. Material & prestress form-finding
Part B · Setup C–E
Plane-stress elasticity + isotropic prestress resultant N_pre
Form-finding: heavily damped dynamics → near-equilibrium before FSI
• MembraneMaterial: Young’s modulus E, Poisson ν, thickness h, prestress
• apply_isotropic_prestress runs MembraneSolver with high damping + mass_scale
• Many small explicit steps; velocities periodically halved, then zeroed
• Purpose: settle fabric under prestress + gravity (dynamic relaxation)
• After form-finding, transient damping is restored from config (may be ~0 for flutter)
• This prestress damping is NOT the same as wanting viscous damping in the FSI run
Tensile Membrane FSI · Partitioned serial-staggered method · 8/26

## Slide 9
7. Fluid grid & solver setup
Part B · Setup F–G
• Uniform Cartesian box: domain L × W × H, resolution nx × ny × nz
• State fields: velocity (u,v,w), pressure p, effective viscosity ν_eff
• Inlet profile tapered near walls to avoid corner spikes
• Optional gust: sinusoidal streamwise + vertical inlet fluctuation
• LES: Smagorinsky SGS adds eddy viscosity when enabled
• Initial IB: membrane_cell_mask marks a thin band of cells as solid
• Solid velocity in masked cells interpolated from nearest membrane nodes
Tensile Membrane FSI · Partitioned serial-staggered method · 9/26

## Slide 10
8. One FSI time step — overview
Part C
Serial staggered loop inside FSISimulation.step() (repeat ≤ max_subiters)
• 1. Update immersed boundary from current membrane x, v
• 2. Advance fluid one Δt (advection–diffusion → pressure Poisson → projection)
• 3. Compute surface loads → nodal forces (× load_scale)
• 4. Under-relax forces if sub-iteration > 0: f ← α f_new + (1−α) f_old
• 5. Set membrane external forces; advance membrane with n_sub substeps
• 6. Measure interface residual from displacement change; break if < tol
• 7. After sub-iters: t += Δt; log disp, KE, CFL, residual, |p|_max
Tensile Membrane FSI · Partitioned serial-staggered method · 10/26

## Slide 11
9. Step 1 — Update immersed boundary
Part C · Detail
• Function: update_immersed_boundary(...) in src/fsi/mesh_update.py
• Build boolean mask of fluid cells near the membrane (thickness_cells ≈ 1.5)
• For each masked cell, find nearest membrane node (in x–y) and copy its velocity
• Pass mask + solid velocity (u_s, v_s, w_s) into FluidSolver.set_immersed_boundary
• During fluid BC application, masked cells are forced to solid velocity
• This is how structure → fluid coupling is enforced (kinematic condition)
• As the membrane moves each step / sub-iter, the mask is rebuilt
Tensile Membrane FSI · Partitioned serial-staggered method · 11/26

## Slide 12
10. Step 2 — Advance the fluid
Part C · Detail
Fractional-step / PISO-like incompressible NS
u* ← advect–diffuse(u) → ∇²φ = (ρ/Δt) ∇·u* → u ← u* − (Δt/ρ) ∇φ
• Convection: first-order upwind; diffusion: Laplacian with ν_eff
• ν_eff = ν_molecular (+ Smagorinsky eddy viscosity if LES on)
• Pressure Poisson with Neumann walls; one cell pinned for uniqueness
• BCs: inlet (profile ± gust), no-slip side walls, zero-gradient outlet, IB force
• Sanitizer clips NaN / runaway velocities (u_clip) on coarse teaching grids
• CFL monitored after the coupled step for diagnostics
Tensile Membrane FSI · Partitioned serial-staggered method · 12/26

## Slide 13
11. Step 3 — Load transfer (fluid → structure)
Part C · Detail
dynamic_pressure
Default teaching model.
Sample fluid vel & p at
element centroids.
Δp ≈ ½ ρ U_n |U_n|
+ 0.3 (p − p∞)
Clip to ±5 q_ref.
Incidence / Bernoulli-like;
good for angled loading.
pressure_jump
Used in flutter.yaml.
Sample p at
centroid ± offset·n
(outside IB band).
Δp = p(−n) − p(+n)
along +normal.
Captures unsteady lift
even when membrane is
aligned with the flow.
interpolated_field
Use interpolated fluid
pressure directly as
surface pressure.
Simplest mapping;
depends on how well
IB pressure is defined
near the membrane.
All modes then scatter
Fe = (p A / 3) n to the
three triangle nodes.
Tensile Membrane FSI · Partitioned serial-staggered method · 13/26

## Slide 14
12. Steps 4–6 — Relax, integrate membrane, residual
Part C · Detail
• load_scale multiplies nodal forces (stabilises coarse / aggressive FSI)
• Under-relaxation (sub-iter > 0): f = α f_new + (1−α) f_old — reduces load oscillation
• membrane.set_external_forces(f_use)
• n_mem = required_substeps(Δt) from membrane critical Δt (wave-speed CFL), capped at 200
• membrane.step(Δt, n_sub=n_mem) advances structure with smaller structural substeps
• Residual ≈ ‖Δx‖ / ‖x_prev‖ between sub-iterations; stop if < residual_tol
• max_subiters = 1 → pure serial stagger (weak coupling); >1 → iterated weak coupling
Tensile Membrane FSI · Partitioned serial-staggered method · 14/26

## Slide 15
13. Membrane dynamics — residual & integrator
Part D
M a = f_ext + f_gravity − f_int(x) − c v
Explicit central difference on free DOFs; fixed edges held at x₀
• f_int = material (Green–Lagrange / plane-stress via CST B matrix) + geometric prestress
• Lumped mass × mass_scale for artificial inertia (larger stable fluid Δt)
• Gravity uses unscaled physical mass so weight is not artificially amplified
• c = damping (Rayleigh-like viscous); set ~0 for persistent flutter
• Safety: clip runaway nodal displacements; zero velocity on clipped nodes
• critical_dt from max(material, prestress) wave speed and min edge length
Tensile Membrane FSI · Partitioned serial-staggered method · 15/26

## Slide 16
14. Membrane internal forces (per triangle)
Part D
• Build local orthonormal frame (e1, e2, n) from reference triangle X₀
• Project displacements into the local plane → 2D CST B matrix
• Strain ε = B u_loc (Voigt); stress σ = C ε; membrane resultant N = h σ
• Material nodal forces from Bᵀ (N A); map back to 3D via e1, e2
• Add geometric / prestress edge forces from isotropic N_pre
• Assemble to global f_int; residual subtracts f_int from loads + gravity
• Contrast: DOLFINx static script derives residual from total potential energy + SNES
Tensile Membrane FSI · Partitioned serial-staggered method · 16/26

## Slide 17
15. Damping & mass_scale — why they exist
Part D
damping c
Appears only in dynamics: −c v
Dissipates KE; kills mesh-scale
ringing and noisy FSI loads.
NOT required by static load analysis
(energy / SNES equilibrium).
default.yaml: c ≈ 80 (quiet demo)
flutter.yaml: c ≈ 0.02 (oscillations live)
You may set c = 0 if you accept
undamped / more fragile transients.
mass_scale
Multiplies lumped nodal mass for
the explicit integrator.
Slows structural response → larger
stable Δt when coupled to fluid.
Does NOT dissipate energy.
Gravity uses unscaled mass so the
sail weight stays physical.
Trade-off: artificial inertia vs
true membrane dynamics.
Tensile Membrane FSI · Partitioned serial-staggered method · 17/26

## Slide 18
16. LES & immersed-boundary details
Part E
• Smagorinsky: ν_t ~ (C_s Δ)² |S|; ν_eff = ν + ν_t when les.enabled
• Teaching grids often raise molecular ν and may disable LES (--quick)
• IB is a thin volumetric band, not a sharp zero-thickness interface
• pressure_jump offset ≈ 3 Δz samples outside that band for Δp
• Kinematic coupling: fluid velocity in band = membrane velocity
• Dynamic coupling: fluid pressure / dynamic pressure → nodal forces
• No ALE mesh morphing of the fluid grid — Cartesian + mask only
Tensile Membrane FSI · Partitioned serial-staggered method · 18/26

## Slide 19
17. Outer run loop & outputs
Part E
• n_steps = ceil(t_end / dt); each iteration calls FSISimulation.step()
• Callback every save_interval: print diagnostics + write artifacts
• snapshot_XXXXXX.npz — membrane nodes + fluid fields
• membrane_XXXXXX.vtk — open in ParaView
• slice_XXXXXX.png — mid-plane |u| with membrane outline
• history.csv / history.png — displacement, KE, CFL, FSI residual
• membrane_flutter.gif — from examples/run_flutter_gif.py
• Entry points: python main.py [-c config] [--quick]; examples/*
Tensile Membrane FSI · Partitioned serial-staggered method · 19/26

## Slide 20
18. Key configuration knobs
Part E
membrane.*
length, width, nx, ny
thickness, density
youngs_modulus, poisson
prestress
damping, mass_scale
fixed_edges
fluid.* / les.*
domain L,W,H + nx,ny,nz
rho, nu, U_inlet
membrane_x0/y0/z0
gust_amp, gust_freq
u_clip (sanitizer)
les.enabled, Cs
fsi.* / time.*
scheme: serial_staggered
under_relaxation α
max_subiters
residual_tol
load_scale, load_mode
dt, t_end, cfl_max
Tensile Membrane FSI · Partitioned serial-staggered method · 20/26

## Slide 21
19. Flutter demo path
Part E
• config/flutter.yaml: light fabric, soft prestress, near-zero structural damping
• Gusty inflow to seed unsteady lift
• load_mode: pressure_jump for Δp across the sheet
• Clamped on all four edges; oscillations intended to persist
• examples/run_flutter_gif.py writes output/flutter/membrane_flutter.gif
• Committed artifacts: NPZ/VTK snapshots, slices, history, GIF
• Shows the partitioned method can sustain dynamic FSI without heavy damping
Tensile Membrane FSI · Partitioned serial-staggered method · 21/26

## Slide 22
20. Contrast: static DOLFINx load analysis
Part F
DOLFINx + PETSc SNES (your script)
Static nonlinear membrane only
Total potential energy Π(u)
Residual = δΠ; Jacobian = dF/du
Point load with load factor stepping
Small u₃ nudge for geometric stiffness
No mass, no damping, no fluid
Equilibrium: F_int(u) = F_ext
MUMPS / Newton line search
This repo FSI path
Transient partitioned FSI
Separate fluid + structure solvers
Explicit CD structure + PISO fluid
Interface loads each Δt
Optional viscous damping
Artificial mass scaling common
IB kinematic coupling
Teaching / prototyping fidelity
Tensile Membrane FSI · Partitioned serial-staggered method · 22/26

## Slide 23
21. Limits & practical tips
Part F
• Cartesian IB fluid ≠ production unstructured LES / OpenFOAM pipeline
• Explicit membrane Δt limited by wave speed — lower dt or E / prestress if unstable
• Dynamic-pressure load model is approximate; swap load_transfer.py for fidelity
• Raised ν and load_scale are stability aids on coarse grids
• If you remove damping: expect more ringing; reduce dt / mass_scale / load_scale first
• For static design loads, prefer energy-based SNES (DOLFINx) over this transient FSI
• Gmsh helper exists for external unstructured coupling experiments
Tensile Membrane FSI · Partitioned serial-staggered method · 23/26

## Slide 24
22. End-to-end flowchart
Summary
YAML config
→
Build mesh + material
→
Prestress relax
→
Fluid + IB init
→
Time loop FSI.step
→
Write outputs
• Inside FSI.step (sub-iters): IB update → fluid.step → loads → under-relax → membrane.step → residual check
• Membrane subcycles with n_sub from structural CFL while fluid advances with global Δt
• History accumulates time, max displacement, kinetic energy, CFL, coupling residual
Tensile Membrane FSI · Partitioned serial-staggered method · 24/26

## Slide 25
23. Key takeaways
Summary
• Coupling is partitioned & serial staggered — not monolithic
• Two-way link: IB (structure→fluid) + pressure loads (fluid→structure)
• Membrane: CST + prestress + explicit CD; fluid: PISO-like + optional LES
• Damping is optional physics/numerics for dynamics; unused in static SNES analysis
• mass_scale, load_scale, α, sub-iters are the main coupling stabilisers
• Choose load_mode for the physics you care about (incidence vs Δp flutter)
• Use default.yaml for quiet demos; flutter.yaml for near-undamped oscillation
Tensile Membrane FSI · Partitioned serial-staggered method · 25/26

## Slide 26
Questions & next steps
Explore: config/default.yaml · config/flutter.yaml · src/fsi/coupling.py
Run: python main.py --quick | python examples/run_flutter_gif.py
Static loads: use DOLFINx energy / SNES path (no damping required)